## Slide 1
Cardboard
Glass
Metal
Paper
Plastic
Trash
Waste Classification System
On-Device ML Inference · OpenMV RT1062 · TFLite
1
Data Pipeline
Roboflow dataset
6 waste categories
2
Local Training
TFLite quantisation
Classifier + Detector
3
Edge Inference
OpenMV RT1062
Real-time on-device
EE6008 Mini Project · Edge AI · Real-Time Inference

## Slide 2
System Architecture Overview
PHASE 1 — DATA
PHASE 2 — TRAINING
PHASE 3 — DEPLOY & INFER
Roboflow Dataset
universe.roboflow.com
Cardboard
Glass
Metal
Paper
Plastic
Trash
Augmentation
Optional / OpenMV
captured photos
Train /
Val / Test
Classifier Training
Transfer learning (MobileNet/CNN) · Output: trained.tflite
Detector Training
Bounding box localisation · Output: detector.tflite
labels.txt
class lookup
OpenMV RT1062 — On-Device Inference
main.py
reads run_mode.txt
Camera capture
preprocess frame
TFLite inference
trained / detector.tflite
Classify output
class + confidence
Detect output
bounding boxes
Data
Training
Detector
On-device
Output

## Slide 3
Phase 2 — Model Training
All training performed locally — no cloud platforms used
Image Classifier
Transfer learning on MobileNet backbone
Trained on 6-class Roboflow dataset
Int8 post-training quantisation
Optimised for OpenMV memory constraints
Output: trained.tflite
Object Detector
Bounding box regression head added
Localise waste items in frame
Quantised to TFLite compact format
Outputs class label + bounding box
Output: detector.tflite
labels.txt — Shared class name lookup

## Slide 4
Phase 3 — On-Device Inference
OpenMV RT1062
Mode switcher
main.py
launcher script
run_mode.txt
"classify" or "detect"
Camera capture
Live frame acquisition
& preprocessing
TFLite inference
trained.tflite or
detector.tflite
Confidence filter
Threshold check
filter low-confidence
Overlay output
Class label +
bounding boxes
Classification mode
Displays class probabilities as on-screen overlay
Prints results via serial output
Top-1 prediction shown with confidence score
Detection mode
Draws bounding boxes around waste items
Labels each detection with class name
Multiple items detected per frame